Ethernet over Coax/RJ-11 (EOC-0102H Series)

- Description

The EOC-0102x-E is the best partner for you to enjoy Internet audio and video entertainment ! Provide the Gigabit speed dual port network interface you can easily access through TV or Phone jack. Do not have to worry about WIFI wireless signal blocking problem.

Every in-home coax or phone jack can be a home AV network connection

EOC-0102H provides two interface of Coaxial and Phone for home networking more easy. Have a high-speed the GIGA network interface, the transmission provides smooth HD high-definition video streaming transmission quality.  Just using the EOC-0102H connected TV/phone in the room on the wall socket outlet. Additional network equipment connected via a network cable. Plug & Play design. Allows you to instantly enjoy high-speed, high-quality audio and video streaming services. A Versatile of network applications and smooth online gaming experience. Whether you are in the living room or den can enjoy anytime, anywhere EOC-0102H convenience as well as ultra-high-speed network transmission speed.

- Features

- Every in-home coax or phone jack can be a home AV network connection.

- High-Speed 224Mbps communications link over existing Coaxial/Copper Cable

- 192Mbps@ up to 700 meters(2,296feet), reach down to 128Mbps @ about 900M(2,952feet)

- Operates transparent to high layer protocols such as TCP/IP

- Auto-MDIX and Auto-sensing 10Base-T or 100Base-TX and Full or Half-Duplex on the Ethernet port and 1000Base-TX Full-duplex

- Plug and Play design for simple installation

- Status LEDs for simple monitoring of the device and connection status

- Parameterized and prioritized quality of service (QoS) guarantees the delivery of high priority packets in the presence of best effort data streams.

- Number of Endpoints does not affect the total system bandwidth of the network.

- Applications

- Extend LAN connectivity to a remote site or between buildings.

- Connect Ethernet over the different Room over existing house’s Coaxial/Phone infrastructure

- Extend WIFI wireless signal reception is poor places through Coaxial/Phone wire.

- Advantages

# Easy for Plug & Play design

EOC-0102H allows you to easily convert TV /phone line in the home as part of the home network. So that you can easily to any corner of the home network, extends the home through the EOC-0102H Plug and Play. And let high-definition digital TV, Blu-ray players, personal computers, wireless AP and other network devices to easily connect to the Internet. The main goal of EOC-0102H is to enable consumers to access, store, and share a wide variety of content around the home without having to install new wiring. This includes broadband data, HD programs, video-on-demand (VOD), multi-room HD DVR recordings, voice over IP (VoIP), and streaming of HD video, music, and photos.

# Enjoy stable and smooth HD video transmission and gaming experience

The design of new EOC-0102H has IEEE802.3ab network transmission standard, provides a more high-performance network, so you can also enjoy the services of high quality audio and video streaming, multiplayer gaming and Internet swim.

# QoS mechanisms to strengthen the quality of media streaming

With advanced QoS features to improve the service quality of multimedia streaming applications. Such as triple-play (data, voice and video) services, high-definition video streaming, VoIP and high-speed Internet access.

# Energy-saving design, reducing energy consumption

Engrgy-saving & Low-power design, when no data access and connection, EOC-0102H will automatically enter a power-saving mode to reduce energy consumption by 40%.

# Hybrid-Link capacity of the transmission medium

EOC-0102H can also use coaxial cable and telephone lines for transmission capacity. Let your home network installation more convenient.

- Technical Specification

- Standards

- IEEE802.3 10BASE-T, 10Mbit/s

- IEEE802.3u 100BASE-TX, Fast Ethernet at 100Mbit/s, Auto-negotiation

- IEEE802.3ab 1000BASE-T

- IEEE802.3x Full Duplex and Flow Control

- Protocol

  - Transparent to High Layer protocol

- Modulation

  - Support QAM, FDQAM

- Encoding

  - CSMA/CA Media Access control

- Frequency Range

  - 12-44MHz

- Transmission Power

  - -2 +/- 1dBm

- Quality of Service

  - IEEE802.1p Priority mapping, IEEE 802.1p/TOS Priority Queue-Based,

  - IEEE 802.1Q Tag VLAN Pass-through

  - Guaranteed QoS based on EOC parameterized QoS

- Connectors

- Gigabit Ethernet：Two RJ45 Connectors

- RJ11：One Female RJ11 Connectors，pin 3~4 for Line，pin1~2 for Phone

- Coax：Two F-Type Female Coax Connectors，One for Line，the other for TV

- Fast Ethernet Interface

  - 10/100/1000 Mbps

  - MDI/MDI-X Auto Crossover

- Power Protection (Surge)

  - IEC 61000-4-2 level 4 (ESD) , 15 kV (air discharge), 8kV (contact discharge)

  - IEC-61000-4-5

  - MIL STD 883G, method 3015-7 Clas 3B, -25kV HBM(human body model)

- Indicators

  - Power LED

  - STB Link/Act LED

  - LAN Link/Act LED

  - Line Link/Sync LED

  - Line Link/Act LED

- Environmental Conditions

  - Operating Temperature ：0 ºC ~ 55 ºC (32 ºF ~ 131 ºF )

  - Storage Temperature： -10 ºC ~ 65 ºC (14 ºF ~ 149 ºF )

  - Operating Humidity：10 % ~ 90 %，Non-condensing

- Power Requirement

  - External Power Supply：12V DC

  - Power Consumption：< 4 Watts

- Dimension

  - 155mm (W) x 83mm (D) x 30mm (H)

- Weight

  - 320g

- Emissions Compliance

  - FCC part 15 Class B, CE Mark

- Performance Table

| Performance : | PHY Link Rate reference Table using 26AWG Copper |
| --- | --- |
|  | Communication distance(feet) | PHY Rate Mbps |
|  | 100 | 224 |
|  | 200 | 224 |
|  | 300 | 224 |
|  | 400 | 192 |
|  | 500 | 192 |
|  | 600 | 192 |
|  | 700 | 160 |
|  | 800 | 160 |
|  | 900 | 160 |
|  | 1000 | 160 |
|  | 1100 | 160 |
|  | 1200 | 128 |
| Performance : | PHY Link Rate reference Table Coaxial |
|  | Communication distance(meter) | PHY Rate Mbps (RG59) | PHY Rate Mbps (RG6) | PHY Rate Mbps (RG7) |
|  | 100 | 224 | 224 | 224 |
|  | 200 | 224 | 224 | 224 |
|  | 300 | 224 | 224 | 224 |
|  | 400 | 224 | 224 | 224 |
|  | 500 | 224 | 224 | 224 |
|  | 600 | 224 | 224 | 224 |
|  | 700 | 192 | 224 | 224 |
|  | 800 | 160 | 224 | 224 |
|  | 900 | 128 | 192 | 224 |
|  | 1000 | 64 | 160 | 224 |
|  | 1100 | NA | 128 | 224 |
|  | 1200 | NA | 64 | 192 |
|  | 1300 | NA | NA | 160 |
|  | 1400 | NA | NA | 128 |
|  | 1500 | NA | NA | 64 |

- Ordering Information

- EOC-0102M-K :  2-port 10/100Base-TX Ethernet over coaxial cable, managed (master unit)

- EOC-0102S-E :  2-port 10/100Base-TX Ethernet over coaxial cable, unmanaged, (slave unit )

- EOC-0102S-K :  2-port 10/100Base-TX Ethernet over coaxial cable, managed, (slave unit)

- EOC-0102H-E :  2-port 10/100Base-TX Ethernet over coaxial cable or RJ-11/Phone line, unmanaged

LED Indications on the Front/Rear Panel :

- Front panel info

| LED | Status |
| --- | --- |
|  | Glowing | Dimming | Flashing |
| Power/PWR | DC 5V Power In | No powered | N/A |
| STB Link/Act | STB Link | Disconnect or Link failed | Receive or Transmit |
| LAN Link/Act | LAN Link | Disconnect or Link failed | Receive or Transmit |
| Coax - Sync mode | Synchronous mode | Green : High Link Speed Red : Low Link speed | N/A |
| Coax - Link/Act mode | Coax/RJ-11 line Link | Disconnect or Link failed | Receive or Transmit |

- Rear panel info

| Port Name | Type | Functions |
| --- | --- | --- |
| DC IN | DC 12V | Connects to the power adapter plug. |
| STB | RJ45 | Connects to Ethernet port on FTTx/xDSL Modem or Switch/AP for Internet Access. |
| LAN | RJ45 | Connects to PC Ethernet port on FTTx/xDSL Modem or Switch/AP for Internet Access. |
| PHONE Line | RJ11 | Pin 3-4 for Line, Pin 1-2 for Phone |
| RF | Coax | Connect to TV |
| Data | Coax | Connects from wall outlet RF in or LINE in or connects to EOC device |

Appendix 1：

Application Diagram

Appendix 2：

Product Comparison Table

|  | Coaxial/Phone Transmission line | PLC Power Transmission line | RJ45 Cable | WIFI Wireless AP |
| --- | --- | --- | --- | --- |
| Connection method | Each socket in the home | Each socket in the home | Computer need RJ45 Cable | Need Wireless Adapter |
| Installation method | Without installation | Without installation | Need Cabling install | Need using computer setting |
| Transmission Distance | 2952ft / 900M | 984ft / 300M | 328ft / 100M | 164ft /50M |
| Electromagnetic waves | Low | Low | Low | Highest |
| Transmission quality | High | High | High | Lowest |
| Extensibility | High | High | Lowest | High |
| Attrition rate | Lowest | Low | High | Highest |
| Anti-interference | High | Low | High | Low |
| Loop leaps and bounds | Support | Non | Non | Non |

# Text boxes

Coaxial /Phone line – Hybrid-Link Ethernet Extender

Note : EOC-0102H-EP : PCBA version only support Coax, no RJ-11 port